## Slide 1: CSC 222: Computer Organization & Assembly Language
Instructor: Anwar Khan
Email:
1 – An Introduction

## Slide 2: Outline
About this Course
Basic Structure of Computer
What is Computer Organization?
About Assembly Language

## Slide 3: What is this course about?

## Slide 4: Course Objectives
To understand organization of a computer system
  To gain an insight knowledge about the internal architecture and working of microprocessors.
  To understand working of memory devices, interrupt controllers and I/O devices.
To learn Assembly Language
  To understand how low level logic is employed for problem solving by using assembly language as a tool.

## Slide 5: Course Contents
Basic Structure & Components of a Computer System
Difference in Computer Organization & Computer Architecture
Computer Evolution
Microprocessor & Microcontrollers
Interconnection Structures
Memory Organization
Data Representation
Instruction Set
Processor Structure & Function
Interrupts
Processor Registers & FLAGS

## Slide 6: Course Contents Contd..
Assembly Language
  Syntax
  Basic Instructions
  Flow Control Instructions
  High Level Language Structures
  Logic, Shift and Rotate Instructions
  The Stack
  Multiplication & Division Instructions
  Array & Addressing Modes
  String Instructions
  Procedures & Macros
  Translation of high level language into assembly language.

## Slide 7: Basic Structure & Function – Computer System

## Slide 8: Structure
Structure is the way in which components relate to each other

## Slide 9: Difference in Peripherals & Communication Lines
When data is received from or delivered by a device that is directly connected to the computer, process is called Input-Output (I/O).
When data are moved over longer distance, to or from a remote device, the process is known as Data Communication.

## Slide 10: Structure - Top Level
Computer
Main
Memory
Input
Output
Systems
Interconnection
Peripherals
Communication
lines
Central
Processing
Unit
Computer

## Slide 11: Structure – Top Level Contd..
Four main structural components:
  CPU: controls the operation of the computer and performs its data processing functions; often referred as processor.
  Main Memory: stores data
  I/O: moves data between the computer and its external environment.
  System Interconnections: Mechanism for communication among CPU, memory, and I/O.

## Slide 12: Structure - The CPU
Computer
Arithmetic
and
Login Unit
Control
Unit
Internal CPU
Interconnection
Registers
CPU
I/O
Memory
System
Bus
CPU

## Slide 13: Structure – The CPU
Control Unit: controls the operation of CPU and hence the computer.
Arithmetic and logic unit: performs the computer’s data processing functions.
Registers: provides storage internal to CPU.
CPU interconnection: Mechanism that provides for communication among the control unit, ALU, and registers.

## Slide 14: Structure - The Control Unit
CPU
Control
Memory
Control Unit
Registers and
Decoders
Sequencing
Logic
Control
Unit
ALU
Registers
Internal
Bus
Control Unit
Notes: Several approaches for CU implementation
1 approach is Micro programmed Control unit which is programmed to execute micro instructions.

## Slide 15: Function
Function is the operation of individual components as part of the structure.
Main functions performed by a computer system are:
  Process Data
  Store Data
  Move Data
  Control the above three functions

## Slide 16: Functional View of Computer

## Slide 17: Possible Operations
Data movement device
Data storage device (read/write)

## Slide 18: Possible Operations Contd..
Processing on data stored in storage or in external environment

## Slide 19: What is Computer Organization?

## Slide 20: Computer Architecture
Computer Architecture refers to those attributes of a system visible to a programmer
  Those attributes that have direct impact on logical execution of a program.
Architectural attributes include:
  the instruction set,
  no. of bits used to represent various data types (numbers, characters etc),
  I/O mechanisms and technology for addressing memory.
Example: Architectural design issue whether a computer will have multiply instruction or not.
Notes: Architecture = Logical aspects
Explain the terms underlined

## Slide 21: What is Computer Organization?
Organization is how features are implemented.
  How does a Computer Work?
    For Example: Is there a special hardware multiply unit for multiplication operation or is it done by repeated addition?
  Computer Organization refers to the operational units and their interconnections that realize the architectural specifications.
  Organizational attributes:
    hardware details transparent to the programmer such as control signals,
    interfaces between peripherals and the computer,
    the memory technology used.
Notes: Organization = physical aspects
How numbers will be multiplied & where result will be stored!

## Slide 22: Computer Organization vs. Architecture
Architecture:
  Logical aspects of computer hardware that are visible to the programmer
    What instruction a computer understands!
Organization:
  Physical aspects of computer hardware that are invisible to the programmer
    How does the computer hardware carries out instructions!

## Slide 23: Computer Organization vs. Architecture Contd..
Computer Organization must be designed to implement a particular architectural specifications.
It is possible to have same architecture but different organizations.
  All computers in the Intel Pentium series have the same architecture.
  Each version of the Pentium has a different organization or implementation.

## Slide 24: Computer Organization vs. Architecture Contd..
Architectural Issues:
  Reduced Instruction Set Computing (RISC)
  Complex Instruction Set Computing (CISC)
  Pipeline etc
Organizational Issues:
  I/O, control unit, memory etc

## Slide 25: Why Study Computer Organization?
Understand how computer works!
  Computer functional components, their characteristics, their performance, and their interactions.
How to select a system?
  Understand tradeoff among various components, such as memory size, CPU clock speed etc.

## Slide 26: Assembly Language

## Slide 27: Computer Level Hierarchy
Figure Reference: http://users.dickinson.edu/~braught/courses/cs251f09/topics/slides/intro.pdf

## Slide 28: Programming Languages
High-Level Languages (HLL)
Assembly Language
Machine Language

## Slide 29: High-Level Language
Allow programmers to write programs that look more like natural language.
Examples: C++, Java, C#.NET etc
A program called Compiler is needed to translate a high-level language program into machine code.
Each statement usually translates into multiple machine language instructions.

## Slide 30: Machine Language
The "native" language of the computer
Numeric instructions and operands that can be stored in memory and are directly executed by computer system.
Each ML instruction contains an op code (operation code) and zero or more operands.
Examples:
Opcode Operand Meaning
-------------------------------------------------
40 increment the AX register
05 0005 add 0005 to AX

## Slide 31: Assembly Language
Use instruction mnemonics that have one-to-one correspondence with machine language.
An instruction is a symbolic representation of a single machine instruction
Consists of:
  label always optional
  mnemonic always required
  operand(s) required by some instructions
  comment always optional

## Slide 32
Sample Program

## Slide 33
Figure: Machine Language Generation by ASM and HLL programs.

## Slide 34: Essential Tools
Assembler is a program that converts source-code programs into a machine language (object file).
Linker joins together two or more object files and produces a single executable file.
Debugger loads an executable program, displays the source code, and lets the programmer step through the program one instruction at a time, and display and modify memory.
Emulator allows you to load and run assembly language programs, examine and change contents of registers. Example: EMU8086

## Slide 35: Why Learn Assembly Language?
Learn how a processor works
  Explore the internal representation of data and instructions
  How to structure a program so it runs more efficiently.
Compilers/Device Drivers/ OS codes
Games/Embedded System