## Slide 1: CSC 222: Computer Organization & Assembly Language
Instructor: Anwar Khan
4 – Processor Basics

## Slide 2: CPU Overview

## Slide 3: Outline
  Basic Operational Concepts
    Processor Clock
    Instruction Representation
    Instruction Cycle

## Slide 4: References
Chapter 1, Ytha Yu and Charles Marut, “Assembly Language Programming and Organization of IBM PC”
Chapter 3, William Stallings, “Computer Organization & Architecture”
Chapter 2, Subrata Ghoshal, “Computer Organization & Architecture”

## Slide 5: Basic Operational Concepts

## Slide 6: Machine Instruction Elements
Each instruction must have elements that contain the information required by the CPU for execution.
These elements can be:
  Operation code: Specifies the operation to be performed (e.g.. ADD, I/O). The operation is specified by a binary code, known as the operation code, or opcode.
  Source operand reference: The operation may involve one or more source operands, that is, operands that are inputs for the operation.
  Result operand reference: The operation may produce a result. Also called destination operand.
  Next instruction reference: This tells the CPU where to fetch the next instruction.
Reference: http://cnx.org/content/m29425/latest/

## Slide 7: Instruction Representation
Within the computer, each instruction is represented by a sequence of bits.
16 bits instruction
  4 bit opcode, 6 bit operand 1, 6 bit operand 2
  4 bit opcode, 12 bit operand
32 bits instruction
64 bits instruction
Figure: A Simple Instruction Format

## Slide 8: Contd..
Binary representations of machine instructions is difficult to remember.
Use a symbolic representation of machine instructions.
Opcodes are represented by abbreviations, called mnemonics, that indicate the operation. Common examples include:

## Slide 9: Instruction Types
Data processing: Arithmetic and logic instructions
Data storage: Memory instructions
Data movement: I/O instructions
Transfer of Control: Test and branch instructions

## Slide 10: No. of Addresses in an Instruction
Three addresses
  Operand 1, operand 2, result
Two addresses
  Source
  Destination
One addresses
  Source or Destination
Zero address
  Zero-address instructions are applicable to a special memory organization, called a Stack. A stack is a last-in-first-out set of locations.

## Slide 11: Types of Operands
Machine instructions operate on data.
The most important general categories of data are:
  Addresses
  Numbers
  Characters
  Logical data

## Slide 12: Basic Operations – Processor
Execute the software by fetching instruction from memory
Look for any external signal and react accordingly
  Input signals from keyboard or mouse etc.

## Slide 13: Processor Clock
Heart of any processor
Simple digital signals at equal time intervals
  Alternate On Off states
All activity within the CPU is synchronized with the edges (rising or falling) of this clock signal.
Reference: http://www.plantation-productions.com/Webster/www.artofasm.com/Linux/HTML/SystemOrganizationa4.html
Rising Edge
Falling Edge

## Slide 14: Program Counter (a.k.a. Binary Counter)
With every falling edge or rising edge (depending upon processor) of clock signal, the counter is incremented by one.
Width varies from processor to processor
The contents of PC are used as target address for the memory area
Microprocessor
Memory
Control Unit (CU)
PC
Data Buffer
Memory
Read
Memory address
Data from Memory
Data
Address
Read
Figure: Reading from memory

## Slide 15: Basic Instruction Cycle
Fetch  Decode  Execute
Fetch
  Fetch an instruction from memory
  Decode the instruction to determine the operation
  Fetch data from memory if necessary
Execute
  Perform the operation on the data
  Store the result in memory if needed

## Slide 16: Contd..
Internal CPU Registers used in instruction cycle:
  Program Counter (PC) = Address of instruction
  Instruction Register (IR) = Instruction being executed
  Accumulator (AC) = Temporary Storage

## Slide 17: Computer Components: Top Level View Contd..

## Slide 18: Detailed Steps
Address in the Program Counter register
  Program Counter (PC) holds address of next instruction to fetch
Fetch the instruction from the memory
Increment the Program Counter
  Unless told otherwise
Instruction loaded into Instruction Register (IR)
Decode the type of instruction
Fetch the operands
Execute the instruction
Store the results

## Slide 19: Example Program Execution

## Slide 20: Instruction Execution Cycle

## Slide 21: Instruction Cycle State Diagram
Notes: Vector data

## Slide 22: Contd..
Instruction Fetch
  Read instruction from memory into processor
Instruction Operation Decoding
  Determine the type of operation to be performed and operand(s) to be used.
Operand Address Calculation
  If operation involves reference to an operand in memory or I/O, then determine the address of operand.
Operand Fetch
  Fetch from memory or read from I/O
Data Operation
  Perform the operation
Operand Store
  Write into memory or out to I/O if required